# USB Protocol description of the Microlife Professional BPA
## Communication protocol
The Microlife BPA uses USB for communication. The device identifies itself as
Bus 002 Device 003: ID 04b4:5500 Cypress Semiconductor Corp. HID->COM RS232 Adapter

and provides two interrupt endpoints.

Bus 002 Device 003: ID 04b4:5500 Cypress Semiconductor Corp. HID->COM RS232 Adapter
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 1.00
  bDeviceClass 0 (Defined at Interface level)
  bDeviceSubClass 0
  bDeviceProtocol 0
  bMaxPacketSize0 8
  idVendor 0x04b4 Cypress Semiconductor Corp.
  idProduct 0x5500 HID->COM RS232 Adapter
  bcdDevice 0.01
  iManufacturer 1 Cypress Semiconductor
  iProduct 2 USB to Serial
  iSerial 0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 41
    bNumInterfaces 1
    bConfigurationValue 1
    iConfiguration 4 Sample HID
    bmAttributes 0x80
      (Bus Powered)
    MaxPower 100mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 2
      bInterfaceClass 3 Human Interface Device
      bInterfaceSubClass 0 No Subclass
      bInterfaceProtocol 0 None
      iInterface 0
        HID Device Descriptor:
        bLength 9
        bDescriptorType 33
        bcdHID 1.00
        bCountryCode 0 Not supported
        bNumDescriptors 1
        bDescriptorType 34 Report
        wDescriptorLength 37
        Report Descriptors:
        ** UNAVAILABLE **
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0008 1x 8 bytes
        bInterval 10
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x02 EP 2 OUT
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0008 1x 8 bytes
        bInterval 10
Device Status: 0x0000
  (Bus Powered)

The communication happens on those two interrupt endpoints, obviosly. It is a low-speed USB device providing 8 bytes of payload on each of the interrupt transfers
## Data format
This describes the plain USB data communication. The encapsulation described in this section is also implemented in the cyrus_m8 kernel driver providing a USB serial console, which simplifies the communication with the device a bit.
### Request
A typical request datagram usually looks like this:
00000000 04 12 16 18 3e 00 00 00 |....>...|

Not much is known about this. Presumably, a high nibble value of all 0 for the first byte denotes a request and the low nibble denotes the payload length as well, but all commands (except switching the user id) are using 04 here. All requests seem to be just one datagram.
### Response
A typical datagram consisting of 8 bytes has the following format:
00000000 f7 33 35 33 30 34 31 33 |.3530413|

The lower nibble of the first byte gives the length of the overall datagram, the high nibble is always F, probably denoting the datagram as a response.
A response can consist of multiple datagrams. To assemble the complete response, all payload data according to the length nibble has to be concatenated into a target buffer.
Unfortunately, a length nibble < 7 does not mean it is the last datagram in the response. Those short datagrams can happen anywhere in the transmission.
After assembling the response, the first byte should be 06 and the modulo 256 checksum of bytes 1 to n-2 should match the value that is hex-encoded in the last two bytes of the response data.
#### Example
Request:
00000000 04 12 16 18 28 00 00 00 |....(...|
Response:
00000000 f3 06 12 16 c0 03 75 08 f6 18 28 32 31 43 42 08 |......u...(21CB.|
The assembled response data then looks like this:
00000000 06 12 16 18 28 32 31 43 42 |....(21CB|
0x12 + 0x16 + 0x18 + 0x28 + 0x32 +0x31 mod 256 = 0xCB which obviously matches.
## Commands
All commands in the section will show the plain serial communication without the USB framing.
### READ_PATIENT_ID
#### Command
Patient ID data is requested using
12 16 18 24
#### Response
00000000 06 34 41 34 37 34 35 34 46 35 32 34 37 39 39 39 |.4A47454F5247999|
00000010 39 39 39 39 39 39 39 2c 30 35 2e 30 30 0d 0a 30 |9999999,05.00..0|
00000020 35 |5|

Bytes 1 – 22 : VersionID which is the patient id plus the padding
Bytes 24 – 29: Version

### READ_CYCLE_DATA
#### Command
Cycle data is requested using the byte sequence
12 16 18 22
#### Response
The (partial) response including the data header and one data set looks like this:
00000000 06 30 30 33 35 30 30 30 31 34 41 34 37 34 35 34 |.003500014A47454|
00000010 46 35 32 34 37 39 39 39 39 39 39 39 39 39 39 30 |F524799999999990|
00000020 30 31 35 30 30 30 30 30 30 30 30 30 30 30 30 30 |0150000000000000|
00000030 30 30 34 36 31 35 38 38 34 30 34 36 31 35 38 38 |0046158840461588|
00000040 34 |4 |

Header data:
Bytes 3 & 4: 33 35 Number of cycles. ASCII-coded hex number 35 = 53 entries
Bytes 9-20 : 34 41 34 37 34 35 34 46 35 32 34 37: Patient id

34	41	34	37	34	35	34	46	35	32	34	37
4A		47		45		4F		52		47
J		G		E		O		R		G

The first set of data starts at byte 33. The data sets are 32 bytes long:

Byte 33 – 42: 31 35 30 30 30 30 30 30 30 30: Date / Time, BCD coded
33/34: Year (last two digits)
35/36: Month
37/38: Day
39/40: Hour
41/42: Minute
If the date was not set on the device, the year is set to 15 and all other date information is left 0.

Byte 43-44: 30 30: Retry Init? This is possibly related to signal arrhythmia detection

Byte 49-56: 30 34 36 31 35 38 38 34: Blood pressure data

Blood pressure data is converted to binary as follows:
- Byte converted from hex char: 30 → 0
- Bits are written into target array MSB → LSB
- First two bits are skipped, the following three 10bit values are converted back to decimal for pulse, diastolic pressure, systolic pressure

30				34				36				31				35				38				38				34
0				4				6				1				5				8				8				4
0	0	0	0	0	1	0	0	0	1	1	0	0	0	0	1	0	1	0	1	1	0	0	0	1	0	0	0	0	1	0	0
		70										86										132

The pressure data is repeated in the following bytes for no obvious reason.